HEDGE TRIMMER SAFETY

- When operating the hedge trimmer, always wear tight-fitting clothing without loose belts, strings, jewelry, etc.

- Always keep a firm grip on both handles.

- Always wear gloves and proper eye and ear protection when operating the hedge trimmer.

- Keep bystanders away (approximately 20 feet) from the working area.

- Never touch or try to stop the moving blades with your hands.

- Always stop the engine before removing anything caught or jammed in the cutting blades.

- Be alert for any objects or materials that could cause an accident or damage the trimmer (wires, fencing, posts, etc.).

- Always keep your body on the carburetor side (back side) of the trimmer and never on the muffler side (front cutting blade side).

- Always place the trimmer on a firm and flat surface when starting the engine.    Never start the trimmer by resting it against your leg of knee.

- Keep clear of the cutting blades at all times.  Blade cutting action begins at the same time the engine starts and will continue until the throttle is returned to the idle position.

- Maintain good balance and footing at all times and do not over-reach.  If you lose your balance and falling is a possibility or if the hedge trimmer slips from your grip, push the trimmer away from your body and let it fall to the ground.  If you attempt to regain control of the trimmer during these situations, the loss of fingers or other serious personal injuries can occur.

- Do not refuel or run the engine in an enclosed area.

- Always turn off the engine and allow it to cool down before refueling.

- Do not smoke or allow open flames or sparks during refueling.

- Do not overfill the tank with fuel.

- Clean up any fuel that may have spilled during refueling before starting the engine.